ROS for Arduino based Robot

# Coordinate System
From http://www.ros.org/wiki/prairiedog:
Following ROS convention, x points out the front of the robot, y points to the left of the robot, and z points up.

# Motors and Quadrature Encoders
Pittman GM8224D201-R2
Mini Gearhead Motor with 500 cnt/rev Encoder
1 to 24 VDC
121 RPM at 6V 140 ma
251 RPM at 12V 175 ma
382 RPM at 18V 200 ma
512 RPM at 24V 220 ma
resistance approx. 4.3 ohms
gear ratio 19.5/1
motor body 1.37" dia. x 3.9" L
3/16" dia. by .7" length shaft
weight 288 grams
$27.50 65 available

## Odometry Parameters
Gear ratio of 19.5 / 1 results in 9750 per wheel revolution
We detect two transitions per encoder count; i.e., 19500 ticks per wheel revolution

Wheels from http://www.servocity.com/html/precision_disk_wheels.html
Diameter: 76.2mm (3”)
Circumference: 239.4mm
Distance per tick: 239.4mm / 19500 = 0.0122764mm